Operations Manual

Item: BV101

Vornado™ Miniature Vortex Mixer

BV101-B

I. Introduction:

The Benchmark Vornado™ Mini Vortex Mixer is a compact, very powerful, vortex mixer designed for vortexing micro tubes of all sizes (0.4ml to 50ml).  It implements dynamic balance technology to provide smooth speed control and quiet operation with low excess vibration.

II. Product Specifications

| Speed: | Fixed: 2800 rpm |
| --- | --- |
| Operation: | TOUCH mix |
| Head: | Rubber cup standard for single tube mixing |
| Dimensions (WxDxH): | 96 x 97 x 64mm |
| Weight: | 0.5kg / 1 lb |
| Electrical: | 100 to 240V, 50-60Hz, 0.6 amps |
| Operating environment: | 4˚ C to 65˚ C |
| Warranty: | 2 years |

III. Product Set-Up:

Place the vortex mixer on a clean, flat, stable surface and press down slightly to allow the feet to adhere. Plug the vortex mixer into a properly grounded outlet.

IV. Product Operation:

Take the tube/vessel to be mixed and pressed downward against the head to activate the vortex mixing action.  When finished mixing, lift the tube upward.

V. Care and Maintenance:

No routine maintenance is required other than to keep the unit clean. Cleaning can be done with a damp cloth.  Avoid the use of solvents as they may attack the rubber cup head or the ABS plastic housing. Do not immerse the mini vortexer in liquid or subject it to temperatures outside of the recommended operating range.

VI. Troubleshooting

| Unit does not turn on. | Ensure that vortexer is firmly plugged into outlet; Check voltage of outlet |
| --- | --- |
| Motor starts slowly | Ensure proper operating temperature |

VII. Service and Contact:

In the event that service or technical support is required, please contact Benchmark by phone at 1-908-769-5555 or by email at info@benchmarkscientific.com.

Also available from :

MyFuge 12

(C1012)

Unlike traditional mini centrifuges, the MyFuge 12 eliminates the need to change rotors when switching between microtubes and PCR strips.  The included, unique COMBI-Rotor is  all that is required for running 12 microtubes and 4 PCR strips simultaneously.

With a fixed speed that produces 2,000 xg, this centrifuge

is perfect for quick spin downs.  Simply close the lid and the unit quickly ramps up to 5500 rpm.  Open the lid, and the rotor quickly decelerates for removal of samples.